## Slide 1: Silvaco Tcad
Presented by : Abdallh Mohamed
Supervisor : Prof. Hani Fikry
Professor of Solid State Microelectronics
ECE Dept. – Faculty of Engineering

## Slide 2: outline
DeckBuild
Atlas
Athena
…..etc

## Slide 3: Deckbuild
Simulation Environment GUI Based
U can work with all Silvaco programs with one of two modes
Batch mode, terminal “Linux Only”
Under deckbuild envi.

## Slide 4: Atlas
Device Simulation
Proof of concept
Characterization “ IV , CV ”
Parametric extraction, “ SS, Ion, Ioff, Vth,… ”

## Slide 5: Athena
Process Simulation
Athena is a process simulator that provides general capabilities for numerical, physically-based, two-dimensional simulation of processes used in semiconductor industry (ion implantation, diffusion, oxidation, physical etching and deposition, lithography,…) “ Verification ”.
Process parameters extraction, “ XJ, Vth, Material thickness… ”

## Slide 6: Athena
Athena simulation
Generating Athena input file
Running Athena simulation
Analyzing Athena output file
Athena input file
It is a text file that can be arranged by using Deckbuild or any text editor.
It collects a sequence of commands (statements) corresponding to the individual steps of a process flow and control commands specified to select physical models and parameters.

## Slide 7: Athena
Athena output file
The main Athena output is the Standard Structure File, a universal file format used by Silvaco simulation programs. The STRUCTURE statement of
Athena creates a Standard Structure File (.str), which contains mesh and solution information, model information, and other related parameters.
Athena to continue process simulation
Atlas or other device simulators to perform electrical analysis
Tonyplot to graphically display the structure created by Athena

## Slide 8: Athena
A process simulation problem must be specified in the:
a) output file
b) input file
c) Standard Structure File

## Slide 9: Athena
The simulation problem must be specified in the input file, defining the following steps:
Initial geometry
Simulation grid
Initial substrate
Sequence of process steps
Epitaxial growth, Layers deposition ,Geometrical etching, Ion implantation, Diffusion,…..etc
Physical models
Implant models, Diffusion models, Oxidation models

## Slide 10: Athena
A process simulation statements must be specified in the:
a) output file
b) input file
c) Standard Structure File

## Slide 11: Athena
Basic operations to create the input file
  Developing a good simulation grid
  Defining initial substrate
  Performing layer deposition
  Performing geometrical etching
  Performing ion implantation and diffusion
  Specifying the electrodes
  Saving the structure file

## Slide 12: Athena
Follow me.
File , examples.
Commands.
Other tools and interface.

## Slide 13: Athena
  #"-P No.of cores“ saves time
  go athena simflags="-P 4"
  LINE X LOC=0.00 SPAC=0.1
  LINE X LOC=0.3 SPAC=0.02
  # INITIAL SILICON STRUCTURE
  INIT SILICON C.BORON=3.0E14 ORIENTATION=100 TWO.D

## Slide 14: Athena
Mesh grid initialization.
Substrate initialization.

## Slide 15: Athena

## Slide 16: Athena
The simulation grid:
a) should be uniform in all device regions
b) has direct influence on simulation time
c) must not be necessarily defined in the input file

## Slide 17: Athena
Performing Gate Oxidation
Next, we will grow an gate oxide layer on the Silicon surface by performing dry oxidation at 950 C for 11 minutes in 3% HCL at 1 atmospheric pressure. To perform this gate oxidation step, from the ATHENA Commands menu, select the items Process Diffuse....

## Slide 18: Athena
Performing Gate Oxidation
Extract tox by two ways : optimizer or trial and error.
Performing Ion Implantation
Boron with a dose of 9.5 x 10exp11 cm-2 at an energy of 10 keV, with the ion beam tilted at 7 and rotated at 30.
Rotation? Due to shadow effect, follow board.

## Slide 19: Athena
Performing Conformal Deposition for Polysilicon Gate
Knowing that the polysilicon layer thickness grown in the NMOS process is 2000 Angstroms, it is possible to substitute this with conformal polysilicon deposition. To set the conformal deposition step, from the ATHENA Commands menu, select the items Process ⇒Deposit⇒ Deposit....
Oxidation.
Poly impl
etchpoly

## Slide 20: Athena
The diffusion step:
a) doesn’t allow to specify a mixture of oxidants
b) can be performed only after an implant step
c) requires time and temperature to be specified

## Slide 21: What is problem here?

## Slide 22: Athena
The implantation step:
a) must always be performed in 2D mode
b) can be performed only on crystalline silicon
c) requires the specification of implant dose and energy

## Slide 23: Athena
To simulate a diffusion step, in oxidizing ambient after a
high dose implant, the diffusion model to set is:
a) Fermi or Two Dimensional
b) Two Dimensional or Fully Coupled
c) Fully Coupled

## Slide 24: Atlas
Extraction
extract name="Ioff" min(curve(v."gate", i."drain"))
extract name="Ion" y.val from curve(v."gate", i."drain") where x.val=1
extract name="Ion/Ioff" (y.val from curve(v."gate", i."drain") where x.val=1) / min(curve(v."gate", i."drain"))
# SS:
extract name="subvt" 1.0/slope(maxslope(curve(abs( v."gate"),log10(abs(i."drain") ))))

## Slide 25: Atlas
Extraction
### P-channel DIBL Test : Returns Vt with 0.1 and 3 volts Vd ## and a DIBL Parameter ####
# extract the next device parameter wuth the drain now at 3 volts....
extract init inf=“ “ # put ur file name here
extract name="pvt2" x.val from curve(abs(v."gate"),abs(i."drain")) where y.val=0.1e-6
# Calculate a DIBL parameter....in V/V
extract name="pdibl" ($"pvt1"-$"pvt2")/(3.0-0.1)
#### Nmos DIBL Test : Returns Vt with 0.1 and 3 volts Vd ####
# extract the next device parameter with the drain now at 3 volts....
extract init inf=“ “ # put ur file name here
extract name="nvt2" x.val from curve(abs(v."gate"),abs(i."drain")) where y.val=0.1e-6
# Calculate a DIBL parameter....in V/V
extract name="ndibl" ($"nvt1"-$"nvt2")/(3.0-0.1)

## Slide 26: Atlas
Save a structure file while Athena is still the active simulator. For example:
STRUCTURE OUTF=nmos.str
Start Atlas with the go atlas command written in the same input deck, This will automatically load the most recent structure from Athena into Atlas.
If you need to load the structure saved into Atlas without using the auto-interface capability, use the MESH command. For example:
MESH INF=nmos.str